## Slide 1: Acoustic Assessment: SPYDR
Hilary Gallagher
711HPW/RHWS
1 July 2022

## Slide 2: Acoustic Assessment
This study was a direct comparison of legacy earcups and SPYDR earcups worn in combination with the HGU-55/P flight helmet and oxygen mask. Data collected 28-30 June, 2022.
Continuous Noise Attenuation
  IAW ANSI/ASA S12.6, Method A
  Methods for Measuring the Real-Ear Attenuation at Threshold (REAT) of Hearing Protectors
  10 subjects
Speech Intelligibility
  IAW ANSI/ASA S3.2, Modified Rhyme Test (MRT)
  Method for Measuring the Intelligibility of Speech Over Communication Systems
  6 subjects
  AIC-25 aircraft communication system
  105 dBA noise environment

## Slide 3: Continuous Noise Attenuation Results
Earcup Configuration |  | Frequency (Hz) |  |  |  |  |  |  | NRSA | 
 |  | 125 | 250 | 500 | 1000 | 2000 | 4000 | 8000 | 80% | 20%
Legacy | Mean | 13 | 14 | 21 | 31 | 35 | 44 | 48 | 20 | 30
 | SD | 8 | 4 | 3 | 5 | 6 | 9 | 9 |  | 
SPYDR | Mean | 13 | 13 | 16 | 27 | 31 | 48 | 57 | 19 | 27
 | SD | 3 | 3 | 3 | 3 | 5 | 5 | 2 |  | 
Earcup Configuration |  | NRSG |  |  | 
 |  | -1 | 2 | 6 | 13
Legacy | 80% | 28 | 21 | 15 | 9
 | 20% | 36 | 27 | 22 | 19
SPYDR | 80% | 26 | 19 | 15 | 12
 | 20% | 31 | 23 | 19 | 16

## Slide 4: Speech Intelligibility Results
Speech intelligibility scores were adjusted for guessing, per subject, using the following formula:
An overall mean score was then calculated across all subjects per condition
Earcup Configuration |  | Speech Intelligibility Score (%)
Legacy | Mean | 91
 | SD | 8
SPYDR | Mean | 94
 | SD | 7

## Slide 5: Discussion/Conclusion
Noise attenuation measurements
  The legacy earcup configuration provided more attenuation at 500, 1000, and 2000 Hz when compared to the SPYDR earcup configuration. However, the legacy earcup configuration had drastically larger standard deviations across all frequencies except one (500 Hz).
  To compare pilot noise exposure estimates, the NRSG, 80% was applied to F-15A cockpit noise data (flight condition: cruise, 25,000 FT PA, 580 KIAS). Overall dBA level of 110 with a noise spectral balance of 2.
    Estimated noise level under legacy earcup configuration = 89 dBA
    Estimated noise level under SPYDR earcup configuration = 91 dBA
Speech intelligibility (SI) measurements
  Subjects scored a mean SI performance of 91% with the legacy earcup configuration and a mean SI performance of 94% with the SPYDR earcup configuration.
Overall, based on the acoustic assessment, the SPYDR earcups would be considered an acceptable replacement for the legacy earcups.

## Slide 6: Questions? Comments? Suggestions?